## Slide 1: Determination of Priority Violations Related to Microbiological Contamination in Public, Non-Community Water Systems, or Oregon Very Small Systems or Non-Regulated Water Serving Restaurant

## Slide 2: 5-101.11 What Is an approved system
What does 5-101.11 say
  Drinking water shall be obtained from an approved source that is:
    (A) A public water system;P or
    (B) A nonpublic water system that is constructed, maintained, and operated according to law.P

## Slide 3: 5-102.11 Standards for Nonpublic water systems
What does 5-102.11 say
  Outlines several requirements for
    Sampling
    Reporting
    Public Notice
    Plan Review

## Slide 4: Sampling Periods for Public Water Systems
Surface Water System
  Sample monthly
Year-Round Ground Water System
  Sample quarterly
Seasonal Ground Water System
  Monthly during operation.
  Only TNC and Non-Transient Non-Community - NTNC

## Slide 5: 5-101.11 Failure to Monitor
  Failure to Monitor and Report for Microbial Contaminants (Total Coliform (TC) and/or E. coli
    No confirmed positive total coliform or E. coli violations over the past three years.
      Priority violation if
        Failure to monitor for two consecutive monitoring periods.
    System Has Confirmed TC or E. coli in the last 3 years
      Priority violation
        A single failure to sample as required in the previous sampling period.

## Slide 6: 5-101.11 Failure to Monitor
Determining Compliance
  Current sampling period should not be considered.
  Use previous sampling period/periods

## Slide 7: 5-101.11 Failure to Monitor
Example
  Inspection occurs in the 4th quarter
  Groundwater facility with no maximum contaminant level (MCL) violations in the last three years
    System did not test in either the 2nd or 3rd quarter
      Priority violation
  Seasonal Groundwater Facility with MCL violation in the last three years.
    Failure to monitor during the previous month.
    Priority violation

## Slide 8: Failure to Monitor Required Corrections
  Priority Violations require immediate correction or alternative measures in place.
    Alternative Measures
      If applicable, post a public notice as required by the Drinking Water Rules (OAR 333-061-0042).
      Provide verification from lab that samples have been submitted for analysis.
    Corrective Procedure
      Obtain current lab test that complies within 14 days.
      Results must be reported to Drinking Water Program.

## Slide 9: 5-501.11 Exceeding MCLs for Microbial Contaminants
Exceeding MCLs for Microbial Contaminants as described in OAR 333-61-0030.
  Confirm with the Drinking Water Program (Phone #: 971-673-0405) that the water system has exceeded MCLs for microbial contaminants.
  Determine if any further consultation should occur with the Drinking Water Program and Foodborne Illness Prevention Program.

## Slide 10: Exceeding MCL Required Corrections
Alternative Measures
  If applicable, Post a public notice, as required by DWP rules (OAR 333-061-0042) .
  Develop procedures that eliminate the use of contaminated water for food preparation, utensil washing, employee and patron hygiene, or any other operations deemed to pose a public health risk.
  Develop a schedule for correction of the violation.
Notes: Non-potable water not allowed for hand washing.

## Slide 11: Exceeding MCL Required Corrections
Corrective Procedure
  Operator must have current laboratory analysis indicating compliance with microbiological maximum contaminant levels (MCL) standards.
  Operator must assure that results have been reported to DW.

## Slide 12: 5.101.11 Interruption of required treatment.
Alternative Measures
  Post public notice as required by DWP rules.
  Develop methods to reduce the use of potable water.
  Measure effectiveness of treatment as appropriate, for example, chlorine levels at tap.

## Slide 13: 5-101.11 Interruption of required treatment.
Corrective Procedure
  Re-establish treatment process.
  Provide laboratory analysis confirming compliance with MCL’s. To Drinking Water.

## Slide 14: Questions?