## Slide 1: Radiological Schedules
What when and how

## Slide 2: Agenda
What kinds of schedules are we discussing?
Initial monitoring
Reduced monitoring

## Slide 3: Who has to do Radiological Monitoring?
Only community systems
Monitoring is at the Entry point
Not needed if purchased water only
  Assuming from another community system

## Slide 4: What schedules are we discussing?
3 Analyte Groups
  Gross Alpha
  Combined Radium (226/228)
  Uranium
Units –
  Alpha and Radium are recorded in pCi/L
  Uranium is in mg/L

## Slide 5: Do schedules for all three need to match?
No – schedules and monitoring periods can be unique to each one.
Check “Chemical schedule details” to review the current monitoring period.

## Slide 6: Initial monitoring:
When does initial monitoring occur?
  PWS first becomes a community system
  PWS adds new source
    First sample is often in plan review and associated to the source
    Sometimes waived if drawing from same aquifer – discission of hydrogeologists

## Slide 7: Initial monitoring (cont.)
Length:
  Quarterly monitoring
  How long?
    Either for 2 quarters or 4 quarters depending on results

## Slide 8: Initial monitoring (cont.)
When can they go off quarterly monitoring?
  Only needs 2 samples if the first 2 are both ND
  If not both ND then 4 samples are required
Who makes the schedule change?
  DMCE (specifically Chuck) during violation review.

## Slide 9: Reduced monitoring
Initial monitoring is done – now what schedule?
  Answer: depending on results of all initial monitoring samples:
    All results were ND: 9-year schedule
    Results are detected but less than ½ MCL: 6-year schedule
    Results are between ½ MCL and MCL: 3-year schedule
    At or above MCL – stays on quarterly

## Slide 10: Reduced monitoring (cont.)
Reduced monitoring sample has been collected – does the schedule change?
  Answer: Last sample result determines next frequency:
    Result were ND: 9-year schedule
    Result are detect but less than ½ MCL: 6-year schedule
    Result are between ½ MCL and MCL: 3-year schedule
    Result at or above MCL – quarterly schedule

## Slide 11: Reduced monitoring (cont.)
When and who reviews?
  The regulating agency during the survey – every time

## Slide 12: Reduced monitoring (cont.)
What it the start date of the new schedule?
  Look at chemical schedule details!
  The day after the end of the monitoring period the sample was collected within.
    Example: The reduced monitoring sample was for a period that ends 12/31/2025 – new schedule starts 1/1/2026

## Slide 13: Chem schedule details
If last sample causes a change in frequency look at Samples received:
  If done – new schedule starts day after current MP
  If incomplete - new schedule starts same day as current MP

## Slide 14: Questions:

## Slide 15: Example #1
9 Year
9 Year
9 Year
Notes: Canby Utility – 00157

## Slide 16: Example #2
9 Year
6 Year
9 Year
Notes: City of Antelope - 00042

## Slide 17: Example #3
6 Year
9 Year
6 Year
Notes: Clayton creek MH Estates - 00048

## Slide 18: Other reduced monitoring (if time allows)
SOC – No detects
  6- or 9- years depending on factors
  System do a complicated process that is submitted to hydrogeologists
    This complicated process makes this prohibitive and done by system not by reg staff

## Slide 19: Other reduced monitoring (if time allows)
VOC – Also no detects
  6- year only
  System do a complicated process that is submitted to hydrogeologists
    This complicated process makes this prohibitive and done by system not by reg staff

## Slide 20: Other reduced monitoring (if time allows)
IOC (including Arsenic and NO2)– No results above MCL
  9- year
  Must have 3 rounds of monitoring (new sources resets the clock)
  No Hydrogeologist review needed

## Slide 21: Other reduced monitoring (if time allows)
DBP’s
  Number and frequency for both standard and reduced monitoring is based on population and water type
  See Table 19 in OAR 333-061-0036 (4)(d)
LCR
  Yearly or 3-year schedules
  Number required is based on population
  See OAR 333-061-0036 (10)(c)(B) – note both routine and reduced are here so look at correct list

## Slide 22: Chuck Michael DWS Compliance Officer charles.e.michael@dhsoha.state.or.us