## Slide 1
Jeopardy
Notifying the Public
Spring Partner Training
Kari Salis, PE
DWP Technical Manger
Notes: Created by Educational Technology Network. www.edtechnetwork.com 2009

## Slide 2
Tier 1 PN | Tier 2 PN | Loss of Pressure | CCR | LCR Public Education
100 | 100 | 100 | 100 | 100
200 | 200 | 200 | 200 | 200
300 | 300 | 300 | 300 | 300
400 | 400 | 400 | 400 | 400
500 | 500 | 500 | 500 | 500

## Slide 3: Tier 1 Public Notice for 100 Question:
Once the PWS has been notified of the violation, how long do they have to issue a Tier 1 notice?

## Slide 4: Tier 1 PN for 100 Answer:
Once the PWS has been notified of the violation, how long do they have to issue a Tier 1 notice?
24 hours

## Slide 5: Tier 1 Public Notice for 200 Question:
Which scenarios require a boil water advisory:
Routine EC+, Repeat TC+
Routine TC+, Repeat EC+
Source EC+, Confirmation TC+, Routine TC+
4-log inactivation req’d, chlorinator fails

## Slide 6: Tier 1 PN for 200 Answer: a,b,d
Which scenarios require a boil water advisory:
Routine EC+, Repeat TC+
Routine TC+, Repeat EC+
Source EC+, Confirmation TC+, Routine TC+
4-log inactivation req’d, chlorinator fails

## Slide 7: Tier 1 Public Notice for 300 Question:
True or False:
The phone duty person in the Portland office must speak to a human, either a partner or PWS operator, if data is received that requires Tier 1 notice.

## Slide 8: Tier 1 PN for 300 Answer:
True
The phone duty person in the Portland office must speak to a human, either a partner or PWS operator, if data is received that requires Tier 1 notice.

## Slide 9: Tier 1 Public Notice for 400 Question:
Who is responsible for creating the public notice and checking it meets the rules?
Bonus question: Who determines if the notice should be hand-delivered, posted, or a press release issued?

## Slide 10: Tier 1 PN for 400 Answers:
Who is responsible for creating the public notice and checking it meets the rules?
The PWS (we can help)
Bonus question: Who determines whether the notice should be hand-delivered, posted, or a press release issued?
The PWS (we can help)

## Slide 11: Tier 1 Public Notice for 500 Question:
Which scenarios require a “Do Not Drink” advisory?
Nitrate above 9.9 mg/L
Nitrate above 10.5 mg/L
Arsenic above 35 ug/L

## Slide 12: Tier 1 PN for 500 Answer: b and c
Which scenarios require a “Do Not Drink” advisory?
Nitrate above 9.9 mg/L
Nitrate above 10.5 mg/L
Arsenic above 35 ug/L

## Slide 13: Tier 2 Public Notice for 100 Question:
True or False:
SDWIS issues auto-generated compliance letters to the PWS for chemical MCL violations.

## Slide 14: Tier 2 Public Notice for 100 Answer:
False:
SDWIS issues auto-generated compliance letters to the PWS for chemical MCL violations.
An informal compliance letter will need to be written by the regulator.

## Slide 15: Tier 2 Public Notice for 200 Question:
A routine arsenic result is 15 ppb (MCL = 10 ppb). Is a Tier 2 public notice required?

## Slide 16: Tier 2 Public Notice for 200 Answer:
A routine arsenic result is 15 ppb (MCL = 10 ppb). Is a Tier 2 public notice required?
No. Compliance and public notice requirement are based on the quarterly average. System will need to begin quarterly monitoring.

## Slide 17: Tier 2 Public Notice for 300 Question:
A routine Nitrate result is 15 mg/L (MCL = 10 ppm). Is a Tier 2 public notice required?

## Slide 18: Tier 2 Public Notice for 300 Answer:
A routine arsenic result is 15 ppb (MCL = 10 ppb). Is a Tier 2 public notice required?
While compliance and public notice is based on a single exceedance, nitrate is an acute contaminant so a Tier 1 notice is required.

## Slide 19: Tier 2 Public Notice for 400 Question:
The purpose of a Tier 2 public notice is to…?
Inform customers that their water is not safe to drink
Inform customers of possible health effects and what the system is doing to resolve the problem
Provide incentive for the PWS to resolve the problem

## Slide 20: Tier 2 Public Notice for 400 Answer: b
The purpose of a Tier 2 public notice is to…?
Inform customers that their water is not safe to drink
Inform customers of possible health effects and what the system is doing to resolve the problem
Provide incentive for the PWS to resolve the problem

## Slide 21: Tier 2 Public Notice for 500 Question:
Which actions are required following a Tier 2 Public Notice:
Repeat the PN every three months as long as the violation/situation persists
The PN must be posted for at least 7 days even if the violation/situation persists
Send a copy of the PN in to DMCE
Return to compliance

## Slide 22: Tier 2 Public Notice for 500 Answer: ALL
Which actions are required following a Tier 2 Public Notice:
Repeat the PN every three months as long as the violation/situation persists
The PN must be posted for at least 7 days even if the violation/situation persists
Send a copy of the PN in to DMCE
Return to compliance

## Slide 23: Loss of Pressure for 100 Question:
True or False:
If pressure in a distribution system drops below 20 psi, a boil advisory must be issued.

## Slide 24: Loss of Pressure for 100 Answer:
False:
If pressure in a distribution system drops below 20 psi, a boil advisory must be issued.
Contamination can enter a pipe if there is zero or negative pressure.

## Slide 25: Loss of Pressure for 200 Question:
The requirement to boil during loss of pressure is:
a) A requirement
b) A best management practice
c) Both – it’s complicated

## Slide 26: Loss of Pressure for 200 Answer: c
The requirement to boil during loss of pressure is:
a) A requirement
b) A best management practice
c) Both – it’s complicated
BMPs specify to boil but if a PWS doesn’t want to we can require a Tier 1 as a “situation with significant potential to have adverse effects on human health”

## Slide 27: Loss of Pressure for 300 Question:
Which of the following public notification template must be used:
Ecoli
Loss of pressure
Any clear message that directs customers to boil their water prior to drinking.

## Slide 28: Loss of Pressure for 300 Answer: c
Which of the following public notification template must be used:
Ecoli
Loss of pressure
Any clear message that directs customers to boil their water prior to drinking.
Since this is usually a BMP. Door hangers with simple messages are common.

## Slide 29: Loss of Pressure for 400 Question:
To lift a no pressure boil advisory, the following must have occurred:
Pressure was restored
Area was shock chlorinated
Area was flushed
Coliform sample(s) were absent

## Slide 30: Loss of Pressure for 400 Answer: ALL
To lift a no pressure boil advisory, the following must have occurred:
Pressure was restored
Area was shock chlorinated
Area was flushed
Coliform sample(s) were absent
Note: PWS should advise customers to flush out their own plumbing.

## Slide 31: Loss of Pressure for 500 Question:
True or False:
A boil advisory is still required during planned maintenance when a water system shuts off all customers.

## Slide 32: Loss of Pressure for 500 Answer:
False:
A boil advisory is still required during planned maintenance when a water system shuts off all customers.
If customers are shut off at the meter, they are not at risk of contaminants entering their plumbing. A courtesy notice should still be given.

## Slide 33: CCRs for 100 Question:
True or False:
Only systems serving more than 3,300 people may send all customers via mail or email a link to a website where the CCR is available.

## Slide 34: CCRs for 100 Answer:
False
Only systems serving more than 3,300 people may send all customers via mail or email a link to a website where the CCR is available.
This option is available to all community systems.

## Slide 35: CCRs for 200 Question:
True or False:
Community systems must report results of all special samples in their CCR.

## Slide 36: CCRs for 200 Answer:
False
Community systems must report results of all special samples in their CCR.
Special samples are not representative of water served to customers and therefore do not need to be reported.

## Slide 37: CCRs for 300 Question:
True or False:
The recently passed America’s Water Infrastructure Act requires PWSs serving > 10,000 to send CCRs twice per year.

## Slide 38: CCRs for 300 Answer:
True:
The recently passed America’s Water Infrastructure Act requires PWSs serving > 10,000 to send CCRs twice per year. This begins in 2020.

## Slide 39: CCRs for 400 Question:
True or False:
Non-transient non-community systems are required to post their CCR in conspicuous locations throughout the area served by the water system.

## Slide 40: CCRs for 400 Answer:
False:
Non-transient non-community systems are required to post their CCR in conspicuous locations throughout the area served by the water system.
Only community systems are required to create a CCR.

## Slide 41: CCRs for 500 Question:
Regulators must:
Review and approve each system’s CCR before mailing
Check that CCRs have been submitted on time during the water system survey
Ensure systems send out previous years’ CCRs if past due
None of the above

## Slide 42: CCRs for 500 Answer: b
Regulators must:
Review and approve each system’s CCR before mailing
Check that CCRs have been submitted on time during the water system survey
Ensure systems send out previous years’ CCRs if past due
None of the above

## Slide 43: Public Education for 100 Question:
Public Education is required if an action level is exceeded for:
Lead
Copper
Both

## Slide 44: Public Education for 100 Answer: Lead only
Public Education is required if an action level is exceeded for:
Lead
Copper
Both

## Slide 45: Public Education for 200 Question:
True or False:
EPA recommends water systems notify individual customers of any results over the action level within 30 days.

## Slide 46: Public Education for 200 Answer:
False:
EPA recommends water systems notify individual customers of any results over the action level within 30 days.
This is a requirement! You can check to see if it was done on the Lead and Copper page:

## Slide 47: Public Education for 300 Question:
True or False:
In Oregon, public education materials must be posted at schools served by a community system if the water system exceeded the lead action level.

## Slide 48: Public Education for 300 Answer:
False:
In Oregon, public education materials must be posted at schools served by a community system if the water system exceeded the lead action level.
Lead in school sampling and reporting of results is separate and implemented by ODE.

## Slide 49: Public Education for 400 Question:
Public education must be completed:
Within 60 days of the end of the monitoring period
Within 60 days of the exceedance
By the December 31 of that year

## Slide 50: Public Education for 400 Answer: a
Public education must be completed:
Within 60 days of the end of the monitoring period
Within 60 days of the exceedance
By the December 31 of that year
For systems on an annual or 3-year schedule, by December 10th.
For systems sampling each 6 months, by March 10th

## Slide 51: Public Education for 500 Question:
Public Education must include which of the following elements:
Brochure with required language
Statement on the bill each quarter until RTC
Press release
Choose 3 or more – PSAs, displays, public meetings, direct delivery to multi-family homes

## Slide 52: Public Education for 500 Answer: ALL
Public Education must include which of the following elements:
Brochure with required language
Statement on the bill each quarter until RTC
Press release
Choose 3 or more – PSAs, displays, public meetings, direct delivery to multi-family homes