## Slide 1: OMD Safety Training
Asbestos Awareness

## Slide 2: Outline
Asbestos Awareness
What is Asbestos?
Health Effects of Asbestos
Avoid Exposure
Locations of ACM and PACM
Recognition of Damaged or Deteriorated ACM or PACM
Emergency Response Procedures
Regulatory Requirements
Points of Contact
Questions / Discussion

## Slide 3: What is Asbestos?
Group of 6 naturally-occurring fibrous minerals
found in certain types of rock formations and include:
  Serpentine Group
    Chrysotile (White)
  Amphibole Group
    Amosite (Brown)
    Crocidolite (Blue)
    Anthophyllite
    Tremolite
    Actinolite
Notes: All asbestos occurs naturally in underground deposits.
Of these six types of asbestos, three are commonly encountered in building materials, including:
  Chrysotile (white)
  Amosite (brown)
  Crocidolite (blue)
Asbestos is the generic term for a group of naturally occurring fibrous minerals with high tensile strength, flexibility, and resistance to thermal, chemical, and electrical conditions.
Asbestos fibers can easily become airborne when disturbed. This can happen during use of asbestos products, mining for asbestos or during normal job duties in industries where asbestos was used. Fibers can also become airborne during natural disasters, renovations, or demolition.
Asbestos is still present as contaminants.

## Slide 4: What is Asbestos?
Notes: Many environmental and safety regulations refer to asbestos products as either Asbestos-Containing Materials (ACM) or Presumed Asbestos-Containing Materials (PACM).
The Oregon Department of Environmental Quality (ODEQ) and Oregon Occupational Safety and Health Division (OR-OSHA) define an ACM as any material containing more than 1% asbestos by weight.

## Slide 5: What is Asbestos
Asbestos is often found below applications. (Not a full list)
Building products
Adhesives
Ceiling/Wall texture and ‘popcorn ceiling’
Cement product (siding, roofing shingles)
Floor tile and mastic
Boilers
Pipe insulation
Sprayed-on fire proofing
Brake linings and clutch pads
Notes: Some common types of ACMs include:
Building Products such as:
  Wall and ceiling insulation
  Floor and ceiling tiles and mastic adhesives
  Troweled-on surfacing materials
  Roofing products, roofing felts, flashing, and flues
  Cement roofing, siding and pipes referred to as transite
  Window glazing compound, gaskets, gypsum wall board and joint taping compound, fireproof drapes and curtains.
  Sprayed-on fire proofing and insulation in buildings
  Insulation on boilers, pipes and valves
  Brake linings and clutch pads

## Slide 6: Properties of Asbestos
  Resistant to heat & electrical current
Notes: Characteristics of Asbestos Fibers:
  Virtually indestructible and resistant to chemicals and heat
  Do not evaporate in air, dissolve in water and are not broken down over time
  Superior insulator and has been used in thousands of products
  Break into very small fibers that must be identified using a microscope and may be up to 700 times small than a human hair
  Once released into the air, fibers may remain suspended for hours or days

## Slide 7: Properties of Asbestos
  Resistant to chemicals / Won’t easily break down or dissolve

## Slide 8: Properties of Asbestos
  Tensile strength / Flexible

## Slide 9: Properties of Asbestos
  Easily woven to make fabric
Notes: Historically, many household and industrial items used asbestos to make fabrics.

## Slide 10: Properties of Asbestos
  Absorbs sound / Fire resistant

## Slide 11: Properties of Asbestos
  Cheap to produce
Notes: The snow in the original Wizard of Oz movie was all asbestos.

## Slide 12: History of Asbestos

## Slide 13: Health Effects
Notes: The most common way for asbestos fibers to enter the body is through breathing.
Generally, ACM is not considered harmful unless it is releasing dust or fibers into the air where they can be inhaled or ingested.
Many fibers are trapped in the mucous membranes of the nose and throat where they can be removed, or some may pass into the lungs, or, if swallowed, into the digestive tract. Some fibers may remain permanently.
Exposure to asbestos can cause disabling or fatal diseases
  Asbestosis
  Scarring of lung tissue
  Lung cancer
  Mesothelioma
  Cancerous tumors
  Gastrointestinal cancer

## Slide 14: Health Effects
Risk of related diseases increase with:
  Concentration of exposure (“Dose” Relationship)
  Duration of exposure
  Frequency of exposure
Latency period of ~10-40 years
  Can result in people taking risks with asbestos
  Difficult to identify specific project or job which lead to exposure
Notes: Because asbestos fibers are so resilient, the body cannot break them down or remove them once they are lodged in lung or body tissues. Exposures are known to cause asbestos-related diseases.

## Slide 15: Friable vs. Non-Friable
Friable: material can be easily crumbled or pulverized by hand
Non-Friable: generally bound in a matrix and will not release fibers unless damaged or disturbed. Can become friable!
  Floor tiles
  Cement asbestos
  Asphaltic mastics
Notes: The physical state of ACMs falls into two categories as described below:
  “Friable Asbestos” is any ACM that hand pressure can crumble, pulverize or reduce to powder when dry. Pipe insulation, boiler jackets, and weathered cement building siding are in this category.
  “Non-Friable Asbestos” is any ACM that cannot be crumbled, pulverized or reduced to powder by hand pressure. Vinyl floor tile in good condition may meet this definition, but asbestos fibers could be released by cutting, grinding, or breaking.
Friable asbestos is more hazardous than non-friable asbestos.
ACMs that are non-friable, not damaged and not deteriorated, and that are left alone will not release asbestos fibers unless they are disturbed.
ACMs will become damaged or disturbed and may release fibers by actions including cutting, sawing, breaking, grinding, drilling, buffing, vibration, or weathering from exposure to water or air currents.

## Slide 17: Health Effects

## Slide 18: Lung Cancer
Risk of lung cancer increases with asbestos exposure
  Up to 90x more likely to develop lung cancer if smoking combined with asbestos exposure compared to non-smokers with little to no exposure
  Smoking can inhibit the body’s natural defenses.
Notes: Lung Cancer
  Lung cancer causes the largest number of deaths related to asbestos exposure. The incidence of lung cancer in people who work in mining, milling, manufacturing and use asbestos is much higher than in the general population. Smokers that are exposed to asbestos are about 90 times more likely to develop lung cancer as non-smokers.

## Slide 19: Mesothelioma
Form of cancer manifested on the protective tissue of the lungs, abdomen, and/or heart cavities
More rare, but often fatal
Treatment available, but cure improbable
No documented direct connection between smoking and risk of mesothelioma
Notes: Mesothelioma
  Mesothelioma is a rare form of cancer often occurring in the thin membrane lining of the lungs, chest, abdomen and heart (rarely). Most cases of mesothelioma are linked to asbestos exposure.

## Slide 20: Asbestosis
Chronic non-cancerous lung disease caused by fiber inhalation
  Fibers aggravate lung tissue
  and cause scarring
  Scar tissue prevents lungs from contracting and expanding normally & inhibits oxygen exchange
  Can increase risk of developing lung cancer
Notes: Asbestosis
  Asbestosis is a serious, chronic, non-cancerous respiratory disease. Inhaled asbestos fibers aggravate lung tissues (alveoli) leaving scar tissue, which prevents the oxygen/blood exchange and removal of carbon dioxide.

## Slide 23: Uses & Materials
Used in ~3,000 different materials
Wood, Glass, and Metal are the only non-suspect materials. All other materials should be sampled prior to impact (even newly-installed).

## Slide 24: Uses & Materials
  Intentionally added to product:

## Slide 25: Uses & Materials
  Product contaminated during mining

## Slide 26: Thermal System Insulation (TSI)
  Heating and cooling applications
    pipe, boiler, tank insulation
    Air duct insulation
    chiller/condensate insulation

## Slide 27: Surfacing Materials
Troweled or sprayed-on applications
  Structural steel fire proofing
  Textured applications – “popcorn” ceilings, e.g.
  Stucco
  Plasters

## Slide 28: Miscellaneous Materials
Flooring
Roofing
Wallboard
Mastics
Gaskets
Cement asbestos pipe & sheeting

## Slide 29
Kingsley Bldg. 220
Kingsley Bldg. 220

## Slide 30
Kingsley Bldg. 302 BX
Kingsley Bldg. 229 Theater

## Slide 31: Uses & Materials
Flooring
Floor tiles, mastics, sheet vinyl
Walls
Joint compound, wall texture & coatings
Ceilings
Ceiling tiles, textured ceilings
Other
Pipe & boiler insulation, cement-asbestos pipes
Caulking, roofing, window glazing, electrical components

## Slide 32: Asbestos in the U.S.
> 1 million-significant occupational exposures
  construction
  renovation/remodeling
  general industry
  fire fighters
March of 2024 – EPA ban of on-going uses of Chrysotile
  5 years for chlor-alkali plants to comply
  Bans brake blocks, aftermarket auto components, and other gaskets within six months
Notes: The Environmental Protection Agency (EPA) officially classifies the six asbestiform varieties in the Asbestos Hazard Emergency Response Act (AHERA). Efforts to ban the mineral began in the 1980s. In 1989, the EPA attempted to ban all asbestos-containing products, but the ban was overturned. However, mining in the United States has stopped. The last U.S. asbestos mine, located in California, closed in 2002. Just in 2024, the EPA banned the on-going uses of Chrysotile.
Chlorine plants were given more time to develop a new process or find a new solution.

## Slide 33: Response to Damaged Materials
Response
  Do not attempt to clean up
  Leave the area immediately
  Contact supervisor
  Isolate area (close doors, etc.)
Contact your Operations and Maintenance Manager when damaged suspect materials are discovered
  When you need to confirm the status of a building material
  When you need consultation for abatement or specific project tasks

## Slide 34: Damaged Materials
Notes: Top left- pipe damaged during excavation work
Top right- old roofing materials buried during remodeling in the 70s/80s
Bottom left- Drywall damaged during workplace violence incident
Bottom center- Fireproof door damaged over time, exposing ACM
Bottom right- Asbestos floor tiles

## Slide 35: Visual Asbestos Identification
Age of building: If the building was built before the 1980s, the likelihood of asbestos-containing materials is higher.
Appearance: Look for materials that appear fibrous.
Damage: Look for signs of damage, deterioration, or disturbance. Damaged asbestos is more likely to release fibers.
Notes: Different types of asbestos looks different, each has its own appearance. Other types of non-ACM material can resemble asbestos.
Visual identification not definitive. Only way to 100% confirm asbestos and type is through laboratory testing or through licensed professional.

## Slide 36: ACM

## Slide 37: Avoid Exposure
In order to avoid exposure to asbestos, you must be aware of where ACMs are located in your facilities.
If you are uncertain whether something is ACM, assume it is ACM and do not disturb it until evaluated by an AHERA accredited inspector.
If you or others need to do work that might involve ACM or PACM, coordinate first with your Operations and Maintenance Manager.

## Slide 38: Avoid Exposure
Never do the following to ACM or PACM:
  Drill
  Hammer
  Cut
  Saw
  Break
  Grind
  Sand
  Damage
  Move
  Disturb

## Slide 39: Avoid Exposure
Care of Asbestos-Containing Flooring Material:
  Sanding of asbestos-containing flooring material is prohibited.
  Stripping of finishes shall be conducted using low abrasion pads at speeds lower than 300 rpm and wet methods.
  Burnishing or dry buffing may be performed only on ACM flooring which has sufficient finish so that the pad cannot contact the ACM.

## Slide 40: Locations of ACM and PACM
Asbestos surveys have been completed for OMD Installations and are available through multiple sources including AGI Training Site Managers or Operations and Maintenance Branch Chief or the Construction and Maintenance Manager at Kingsley Field and Portland Air National Guard Base, respectively.

## Slide 41
Are there impacts to something other than wood/glass/metal?
Yes
No
Do I have a Regulated Building Material Survey?
Project Time, Now What?
Yes
No
Yes
Asbestos Identified?
No
Contact AGI Training Site Manager, O&M Branch Chief, or Construction and Facility Maint. Mgr.
Impacts to ACM Required?

## Slide 42: Asbestos Reporting Process
1) Project gets requested through Job Request Form.
2) Authorized Asbestos Management Coordinator conducts necessary survey and submits Maintenance Work Authorization Form to project requester
  Bulk sample if necessary
  3) Approved Contractor (or authorized staff) conducts work with Maintenance Work Authorization on site.
Notes: THIS SLIDE NEEDS TO BE MADE SPECIFIC TO OMD AND SPECIFIC OMD LOCATIONS

## Slide 43: Job Request Form

## Slide 44: Maintenance Work Authorization Form
Notes: THIS SLIDE NEEDS TO BE MADE SPECIFIC TO OMD AND SPECIFIC OMD LOCATIONS

## Slide 45: Expanding Scopes
Carefully review asbestos memo to make sure everything within the Scope is addressed, especially if there are changes.
Call your Point of Contact on the next slide with any questions

## Slide 46: Regulatory Requirements
Oregon Occupational Safety and Health Division:
  OAR 437-002-1910.1001 General Industry
  OAR 437-003-1926.1101 Construction
  OAR 437-005-1915.1001 Shipyards
  OAR 437-004-9050 Agriculture
Oregon Department of Environmental Quality:
  OAR 340-248-0005 Abatement, Licensing, Accreditation

## Slide 47: Regulatory Requirements
U.S. Environmental Protection Agency Laws:
  Asbestos Hazard Emergency Response Act
  Asbestos School Hazard Abatement Reauthorization Act
ORARNGR 385-16
Asbestos Management Plan and Appendices
Notes: Asbestos Hazard Emergency Response Act- Regulates asbestos in schools requiring inspections, management plans and response actions; and accrediting requirements for asbestos inspectors all public (government) and commercial buildings.
Asbestos School Hazard Abatement Reauthorization Act is a Law included the Model Accreditation Plan, which expanded the accreditation requirements to cover asbestos projects in all public (government) and commercial buildings.
Most importantly, we have OR ARNGR 385-16 which details personnel and management responsibilities, training requirements, respiratory protection and medical surveillance programs, notification and record-keeping requirements, and maintenance work practices.

## Slide 48: Points of Contact
Oregon Military Department:
  Tim Gilbert, Chief, AGI – Operations & Maintenance Branch, 503-507-3433 Cell
  Nic Kotz, AGI – Training Site Manager, RTC, 971-453-2184 Cell
  Henry Idica, AGI – Training Site Manager, CRO, 503-508-1367 Cell
  Mike Jones, Construction & Maintenance Manager, Kingsley, 971-719-1161 Cell
  Tod Hyland, Construction & Maintenance Supervisor, PANG, 541-740-9914 Cell
  Steve Wolfe, Deputy Director, OYCP, 971-428-7548 Cell
  Chris Richardson, AGI-Environmental Branch, 971-599-9138 Cell
  Amanda Casteel, OMD Safety Specialist, 503-798-3951 Cell

## Slide 49
QUESTIONS / DISCUSSION